OhmPi installation checklist v1.0.0
Date (YYYY-MM-DD):
Installer:
Location (e.g. Rocherfort (BE), 54.2223, 3.4423):
OhmPi name (register your ohmpi on https://ohmpi.org) :
OhmPi config (e.g. mb2024+4*mux2023+dph5005):
Before going in the field:
- Measurement board
  - Continuity check (SC checks) (power off)
  - Voltage check (power on)
Check shunt resistor, board version and values in config.py
  - Resistance check on reference resistor board with quad [0,0,0,0]
Multiplexer board
All role cables (A, B, M, N) wired to right board/connector and MUX boards addresses match those in config.py
  - Continuity test (OhmPi.test_mux())
  - Resistance check on reference resistor board with reference_sequence file
In the field:
- Immediate surrounding free of power sources that could affect the system (e.g. generator, high voltage line)
- Cables firmly connected to screw terminals (gently pull wires to check connections)
- Metallic enclosure wired to ground
- System protected from rainfall/sun and humidity (sun shade, silicagel, water tight spray, etc.)
- Charged batteries
- Decoupled solar charging system from battery when measuring
Power system:
- Software tests (OhmPi.test())
- Resistance check on reference resistor board with reference_sequence file
Connect your electrodes:
- Contact resistance check
- Sequence run
  - Current does not reach the limit of 4800/50/shunt_value mA (e.g. for a shunt of 2 Ohm, this means a limit of 48 mA)
  - Full-waveform check for noise or strange decay (OhmPi.plot_last_fw())